ICM32 Remote Setup – ICM32 Internet Connection through a Router

# Determine ICM32 LAN IP Address

- The ICM-32 is configured to use DHCP and will automatically obtain an IP address on power-up.

- To find out the address, make sure the speaker volume is up when the unit is powered-on. The ICM32 will announce the IP address over the speaker on power-up.

- Connect the ICM32 to the LAN using rear ethernet connector J7.

- Apply power to the ICM32 to rear jack, and write down the IP address that is announced.

# Set Port Forwarding

- Configure your firewall to forward UDP port 3030 and UDP port 10861 to the ICM32’s LAN IP Address

# Public IP Address

- Send SAS your public IP address so that we can configure the remote end of the connection

- You can find out your public IP address from a computer that is on the same LAN as the ICM32

- From a web browser, go to www.whatismyip.com. It will display your public IP address.

- Send your public IP address to ken@sasaudio.com, and we will set up the remote side to send to your ICM32 station.

Changing ICM32 LAN Address (optional)

- If you need to change the ICM32 address to a fixed IP address, you can do so after you have powered-up the ICM32 on the LAN, and it has obtained a DHCP address.

- Open a web browser on a computer that is also on the LAN, and type in the ICM32’s LAN address in the address bar

- On the ‘SAS Device Setup’ page that is displayed, enter the static IP address into the ‘IP Address’ field under ‘NETWORK SETTINGS’, and hit the ‘Apply’ button.

- The IP address change should take effect after a few seconds.

- To change back to DHCP, follow steps above, and set IP address to 0.0.0.0

fig 1. Changing ICM32 IP address to static 10.0.0.7

NOTE: if the ICM-32 has a fixed IP address that doesn’t match your subnet (ex: it announces a fixed IP address in the 192.168.0.X range, and your network uses 10.0.0.X addresses), you can still connect to it from a PC. Go to start->run, type “cmd”, and in the command prompt window type the following:

route add <ICM32 IP address> mask 255.255.255.255 <your PC's IP address>

You can then enter the ICM32’s IP address in your web browser and get to the configuration page.