CRS-8RJ Connector Pin Out:

9-PIN D (J3) 	DESCRIPTION

- Power ground

### Power ground

- +12VDC

- RS-485+ (Primary)

- RS-485- (Primary)

- Panel Address Bit 0

- Panel Address Bit 1

- Panel Address Bit 3

- Panel Address Bit 2

##### RJ-45 (J1 & J2) 	DESCRIPTION

#### RS-485+ (Primary)

- RS-485- (Primary)

###### Power ground

- Power  (See Note 2)

- Power  (See Note 2)

###### Power ground

- RS-485+ (Auxiliary)

- RS-485- (Auxiliary)

Note 1: 	Apply +12 volts DC using ONLY ONE of J1, J2, or J3.

Note 2:	J1 (J2)-pins 4 & 5 are connected to DS1-Switch 7 (8).

Switch 7 (8) must be ON for J1 (J2)-pins 4 & 5 to be connected to +12VDC.

If Switch 7 (8) is OFF, J1 (J2)-pins 4 & 5 are isolated from +12VDC.

See Switch (DS1) description below.

SWITCH (DS1)	DESCRIPTION

1,2,3,4,5,6	Panel Address Bits 0,1,2,3,4,5 respectively

1,2,3,4,5,6 = OFF,OFF,OFF,OFF,OFF,OFF:	Address = A0

1,2,3,4,5,6 = ON,OFF,OFF,OFF,OFF,OFF:	Address = A1

1,2,3,4,5,6 = OFF,ON,OFF,OFF,OFF,OFF:	Address = A2

1,2,3,4,5,6 = ON,ON,OFF,OFF,OFF,OFF:	Address = A3

- If ON, connects J1-pins 4 & 5 to +12VDC.

- If ON, connects J2-pins 4 & 5 to +12VDC.

## JUMPER (J5)	DESCRIPTION

Placing a jumper on J5 connects +12VDC to J4-pin 4 to provide off-board Auxiliary Power.