ICPM Connector Pin-Out:

Note: The ICPM is used in the Rubicon’s RPB24A, RPB-16A, & RPB-8A, the Rubicon SL’s RSLPB16A & RSL-PB16A, the Rubi-T’s TP-ICM8L, and the CP-16 rack mount panel.

9-PIN D (J4) 	DESCRIPTION

- Power ground

### Power ground

- Power Inlet (+12 to +24 VDC)

- RS-485+ (Primary)

- RS-485- (Primary)

- Panel Address Bit 0

- Panel Address Bit 1

- Panel Address Bit 3

- Panel Address Bit 2

##### RJ-45 (J2, J3, J6, J7) 	DESCRIPTION

#### RS-485+ (Primary)

- RS-485- (Primary)

###### Power ground

- Power  (See Note 2)

- Power  (See Note 2)

###### Power ground

- RS-485+ (Auxiliary)

- RS-485- (Auxiliary)

Note 1: 	Apply +12 volts DC using ONLY ONE of J2, J3, J4, J6, or J7.

Note 2:	J2/J6 (J3/J7)-pins 4 & 5 are connected to DS1-Switch 7 (8).

Switch 7 (8) must be ON for J2/J6 (J3/J7)-pins 4 & 5 to be connected to Power Inlet.

If Switch 7 (8) is OFF, J2/J6 (J3/J7)-pins 4 & 5 are isolated from Power Inlet.

See Switch (DS1) description below.

SWITCH (DS1)	DESCRIPTION

1, 2, 3	Panel Address Bits 0,1,2 respectively

8 addresses max for Intercom/SOC.  4 addresses max for turret/console

1, 2, 3 = OFF, OFF, OFF:	Address = A0

1, 2, 3 = ON, OFF, OFF:	Address = A1

1, 2, 3 = OFF, ON, OFF:	Address = A2

1, 2, 3 = ON, ON, OFF:	Address = A3

1, 2, 3 = OFF, OFF, ON:	Address = A4	(A0 in turret mode)

1, 2, 3 = ON, OFF, ON:	Address = A5	(A1 in turret mode)

1, 2, 3 = OFF, ON, ON:	Address = A6	(A2 in turret mode)

1, 2, 3 = ON, ON, ON:	Address = A7	(A3 in turret mode)

4, 5	Panel Mode

4, 5 = OFF, OFF:	Intercom

4, 5 = ON, OFF:	SOC

4, 5 = OFF, ON:	Turret

4, 5 = ON, ON:	Future use (selects Turret mode for now)

- Alphanumeric Display brightness level

6 = OFF:	Dim (Rubicon)

6 = ON:	Bright (Rubicon SL, Ruby-T)

7	7 = ON: connects J2 & J6 (pins 4 & 5) to Power Inlet.

8	8 = ON: connects J3 & J7 (pins 4 & 5) to Power Inlet.