TP-L4 Connector Pin Out:

9-PIN D (J4) 	DESCRIPTION

- N.C.

### Power ground

- +12 volts DC

- N.C.

- N.C.

- N.C.

- N.C.

- N.C.

- N.C.

##### RJ-45 (J2 & J3) 	DESCRIPTION

#### RS-485+ (Primary)

- RS-485- (Primary)

###### Power ground

- +12 volts DC

- +12 volts DC

###### Power ground

- RS-485+ (Auxiliary)

- RS-485- (Auxiliary)

Note 1: 	Apply +12 volts DC using ONLY ONE of J2, J3, or J4.

Note 2: 	+12 volts DC  and Power ground is always present at J2 & J3 (pins 3-6), even if J4 is used to supply the power.

SWITCH (DS1)	DESCRIPTION

1,2	Panel Address

1,2 = OFF, OFF:	Address = A0

1,2 = ON, OFF:	Address = A1

1,2 = OFF, ON:	Address = A2

1,2 = ON, ON:	Address = A3

3,4	Operational Mode

3,4 = OFF, OFF:	TP-L4 mode

3,4 = ON, OFF:	Rubicon SL Input Module Mode (Shipping Mode)

3,4 = OFF, ON:	Test mode for Buttons and LEDs

3,4 = ON, ON:	Test mode for Fader and S/W version

5,6,7,8	Not Used