CP-16 Connector Pin-Out:

9-PIN D (J4) 	DESCRIPTION

- Power ground

### Power ground

- Power Inlet (+12 to +24 VDC)

- RS-485+ (Primary)

- RS-485- (Primary)

- Panel Address Bit 0

- Panel Address Bit 1

- Panel Address Bit 3

- Panel Address Bit 2

##### RJ-45 (J2/J3/J6/J7) 	DESCRIPTION

#### RS-485+ (Primary)

- RS-485- (Primary)

###### Power ground

- Power  (See Note 2)

- Power  (See Note 2)

###### Power ground

- RS-485+ (Auxiliary)

- RS-485- (Auxiliary)

Note 1: 	Apply +12 volts DC using ONLY ONE of J2, J3, J4, J6, or J7.

Note 2:	J2/J6 (J3/J7)-pins 4 & 5 are connected to DS1-Switch 7 (8).

Switch 7 (8) must be ON for J2/J6 (J3/J7)-pins 4 & 5 to be connected to Power Inlet.

If Switch 7 (8) is OFF, J2/J6 (J3/J7)-pins 4 & 5 are isolated from Power Inlet.

See Switch (DS1) description below.

SWITCH (DS1)	DESCRIPTION

1, 2	Panel Address Bits (4 addresses max)

1, 2, = OFF, OFF:	Address = A0

1, 2, = ON, OFF:	Address = A1

1, 2, = OFF, ON:	Address = A2

1, 2, = ON, ON:	Address = A3

3, 4, 5, 6	Mode of Operation

3 = ON:	SOC Mode (always bright display)

4 = OFF:	Button presses set to TAKE

4 = ON:	Button presses set to SUM

5, 6 = OFF, OFF:	“HOT TAKE”, Panel armed

5, 6 = ON, OFF:	“ENABLE”, requires button press to arm

3, 4, 5, 6 = all other combos:	Reserved for future use

7	7 = ON: 	Connects J2/J6 (pins 4 & 5) to Power Inlet

8	8 = ON: 	Connects J3/J7 (pins 4 & 5) to Power Inlet