Turret and Desk Mounted Studio Panels Connector Pin Out (CRS-8 processor)

The Turret and Desk mounted Studio Panels provide microphone control, pushbutton selection, delay control, monitor selection and volume control, talkback/IFB and intercom functions.  Up to four panels can be connected in parallel on one RS-485 communication port in a ‘party-line’.  Each panel must be strapped to respond to a different address when connected on a common port.

The panels require a 12 VDC regulated power supply, which is wired on the 9 pin Dsub interface connector.  One SAS TP-CS power supply will power up to 4 modules.

The SAS RS-485 port to which the Turret type Button panels and Monitor panels are connected must be programmed to be ‘console type’ from the RCS Router Control Software.  The port will then allow you to program each button for the desired function.

The port to which Intercom button panels are connected must be programmed to be ‘intercom’ type from the RCS.

9-PIN D Fem 	DESCRIPTION

(male on panel, female cable connector)

- RS-485 signal ground / Address ground

- Power ground

- +12 volts DC

- + RS-485 positive signal

- - RS-485 negative signal

- Panel Address Option A

- Panel Address Option B

- Panel Address Option C

- Panel Address Option D

## Addressing Options

# A0	Do not jumper

A1 	Jumper pin 6 to pin 1 (Gnd)

A2	Jumper pin 7 to pin 1 (Gnd)

A3	Jumper both pins 6 and 7 to pin 1 (Gnd)